## Slide 1
Data book
BL series of ceiling AP
BL 290X
Document version number: V1.0
Copyright©2020 Shuotian Information Technology Co., Ltd. All rights reserved

## Slide 2
Power and responsibility statement
No content of this publication may be reproduced, disseminated, transcribed, stored in a retrieval system, or translated into any human or computer language, in any form or by any means, without the written permission of the Company. The use of unauthorized copies of products not only infringes copyright but may prevent Shuotian Information Technology from providing accurate and up-to-date information to users and operators.
is the trademark of Shenzhen Shuotian Information Technology Co., Ltd. All other trademarks, product logos and trade names mentioned in this manual are the property of their respective owners.
The content of this manual is subject to change due to product version upgrade or other reasons. Shuotian Information Technology Co., Ltd. reserves the right to modify the content of this manual without any notice or prompt. In laws and regulations allow range, day to recognize Shuotian information technology co., LTD., in any case, all wrong because of the use of this product manual or this website content and cause of the accident, negligence, contract damage, defamation, copyright or intellectual property infringement and any special, incidental, indirect, secondary loss compensation, no any profits, data, and to compensate the loss of goodwill or anticipated savings, also does not assume any legal liability.
Security statement
Please read the safety and compatibility information of the product before powering it up.
Environmental statement
The product conforms to the design requirements of environmental protection. The storage, use and disposal of the product shall comply with the requirements of relevant national laws and regulations.
Revision record
The revision record accumulates the notes for each manual update, and the latest version of the manual contains all previous manual updates.
www.sailskywifi.com

## Slide 3
Directory
1. Product characteristics·····························································4
2. Packing list·················································································5
3. Application scenarios································································6
4. System information ··································································8
5. Gigabit Ethernet port································································8
6. Radio··························································································9
7. LED···························································································11
8. Power supply···········································································11
9. Environmental parameters ····················································11
10. Certification············································································12
11. Other connectors and designs ··············································12
12. Contact information······························································12
www.sailskywifi.com

## Slide 4
BL290X - Wireless access point
BL290X is a dual band dual concurrent 2x2 series enterprise WLAN access point.
The BL290X series enterprise access point should provide the following:
- Integrated antenna
- A 5GHZ2X2802. 11AX radio subsystem and a 2.4GHZ2X211N radio subsystem
- Five Gigabit Ethernet ports
- 5G module
- Powered from within the standard 802.3AF power supply on the 1000BASE-T port and external power adapter
01
Product characteristics
www.sailskywifi.com

## Slide 5
02
Packing list
www.sailskywifi.com
BL290X ×1
Power adapter×1（48V0.5A)
Cable×1
（1 meter）
Product specification×1

## Slide 6
1. Office, classroom and other indoor places
03
Application scenarios
2. Shopping malls, supermarkets and other places
www.sailskywifi.com

## Slide 7
3 . Restaurants, cafes and other places
4. Hotel and other places
www.sailskywifi.com

## Slide 8
System information | 
Product Description | IEEE 2x2 11n/ac/ax dual band dual concurrent access point
CPU | MediaTek MT7621A MIPS1004Kc(880MHz)
RF | 2.4g&5g：mt7915dn
Gigabit PHY | Integrated with MT7621A
Flash Memory | 16MBx1SPI NOR flash
DDR Memory | DDR3256MB1200Mbps
Power consumption | 1000mW
04
System information
www.sailskywifi.com
05
Gigabit Ethernet port
Gigabit Ethernet port | 
Gigabit Ethernet | LAN1: 10/100/1000 auto-sensing (MDI/MDX) RJ-45 WAN1: 10/100/1000 auto-sensing (MDI/MDX) RJ-45
POE | LAN1&WAN1: Gigabit port operate as a powered device (PD) within standard 802.3at/af Power Over Ethernet from either a mid or end span power source equipment (PSE).

## Slide 9
Radio | 
1x2x2bgn 2.4GHz Radio subsystem | -IEEE 802.11b/g/n/ac/ax MIMO 2x2 2.4~2.4835 GHz -Modulation IEEE 802.11b/g: DSSS (DBPSK, DQPSK, CCK) OFDM (BPSK, QPSK, 16-QAM, 64-QAM) IEEE 802.11n: OFDM (BPSK, QPSK, 16-QAM, 64-QAM) IEEE 802.11ac: OFDM (BPSK, QPSK, 16-QAM, 64-QAM, 256-QAM) IEEE 802.11ax: OFDM (BPSK, QPSK, 16-QAM, 64-QAM, 256-QAM,1024 -QAM) -Channels IEEE802.11b/g: operation in channels 1-14 IEEE 802.11n: HT20 and HT40. -Data rate: IEEE 11b: 11/5.5/2/1Mbps IEEE 11g: 54/48/36/24/18/12/9/6Mbps IEEE 11n: 20MHz: 6.5Mbps~144.44Mbps 40MHz: 13.5Mbps~300Mbps IEEE 11ac: 20MHz: 6.5Mbps~173.3Mbps 40MHz: 13.5Mbps~400Mbps IEEE 11ax: 20MHz: 8.6Mbps~286.8Mbps 40MHz: 17.2Mbps~573.5Mbps TX Power: 19dBm (max) (detail see table)
06
Radio
www.sailskywifi.com

## Slide 10
www.sailskywifi.com
07
LED
LED | 
WPS | Green LED
WIFI(2.4gled/5gled) | Green LED
BT | Green LED
WAN/LAN | Green LED
08
09
Power supply
Environmental parameters
LED | 
DC power adapter | 100~240VAC, 50/60Hz input, Output: 12V/1.5A
PoE | 802.3at 48VDC PoE
Environmental parameters | 
EMI | -FCC part 15 Class B -CE
Safety | -ul60950-1 -EN60601-1-2 Medical (TBD)
Temperature | -0 to 40 degrees C ( Operating Temperature) -20 to 70 degree C (Storage Temperature)
Operating humidity | 5% to 95% (Noncondensing)
Non-Operating humidity | 5% to 95% (Noncondensing)

## Slide 11
Authentication | 
Authentication | CCC，SRRC，CE，FCC
National Customer Service Number ：0755 - 27209470
Shenzhen Shuotian Information Technology Co., Ltd
5B-18, Shenzhou Computer Building, No.2 Beier Road, Longgang District, Shenzhen
www.sailskywifi.com
10
Authentication
11
Other connectors and designs
Other connectors and designs | 
5G Mobile Networks | USB 3.0BUS M.2_B-KEY (Built-in Micro SIM CARD) The support mode depends on the module connected
Reset/WPS Key | SW reset
Size | 260mm*220mm*45mm
Weight | 0.65kg

## Slide 12
Copyright©2020 Shuotian Information Technology Co., Ltd. All rights reserved