## Slide 1
Datasheet
BL series
BL608X
File version: V1.0
Copyright©2020 SHENZHEN SHUOTIAN INFORMATION TECHNOLOGY CO., LTD., all rights reserved

## Slide 2
Power and responsibility statement
No content of this publication may be reproduced, disseminated, transcribed, stored in a retrieval system, or translated into any human or computer language, in any form or by any means, without the written permission of the Company. The use of unauthorized copies of products not only infringes copyright but may prevent Shuotian Information Technology from providing accurate and up-to-date information to users and operators.
is the trademark of Shenzhen Shuotian Information Technology Co., Ltd. All other trademarks, product logos and trade names mentioned in this manual are the property of their respective owners.
The content of this manual is subject to change due to product version upgrade or other reasons. Shuotian Information Technology Co., Ltd. reserves the right to modify the content of this manual without any notice or prompt. In laws and regulations allow range, day to recognize Shuotian information technology co., LTD., in any case, all wrong because of the use of this product manual or this website content and cause of the accident, negligence, contract damage, defamation, copyright or intellectual property infringement and any special, incidental, indirect, secondary loss compensation, no any profits, data, and to compensate the loss of goodwill or anticipated savings, also does not assume any legal liability.
Security statement
Please read the safety and compatibility information of the product before powering it up.
Environmental statement
The product conforms to the design requirements of environmental protection. The storage, use and disposal of the product shall comply with the requirements of relevant national laws and regulations.
Revision record
The revision record accumulates the notes for each manual update, and the latest version of the manual contains all previous manual updates.
www.sailskywifi.com

## Slide 3
Directory
1. Product characteristics·····························································4
2. Packing list·················································································5
3. Application scenarios································································6
4. System information ··································································8
5. Gigabit Ethernet port································································8
6. Radio··························································································9
7. LED···························································································11
8. Power supply···········································································11
9. Environmental parameters ····················································11
10. Certification············································································12
11. Other connectors and designs ··············································12
12. Contact information······························································12
www.sailskywifi.com

## Slide 4
BL608X - Wireless Access Point
BL608X is a high-performance, high-speed indoor 11ax dual-band ceiling AP. It uses a professional industrial-grade Qualcomm chip to provide 2.4GHz and 5.8GHz dual-band wireless services. It comes with 2 Gigabit WAN/LAN ports ( SFP is optional), the maximum wireless rate can reach 3000Mbps, the wireless environment is cleaner, the wireless access is more stable, the wireless access users are more, and the wireless rate is faster. Access provides a great solution. The 2.4G and 5G dual-band WIFI of this PCB board are equipped with 2 sets of independent signal amplifiers (PA and LNA) respectively, using an omnidirectional 5dBi high-gain antenna, which has a longer wireless coverage distance and a stronger ability to penetrate walls; it also supports intelligent channel analysis. And automatically select the optimal channel, reduce interference and delay, and provide a stable wireless network signal. In addition, BL608X supports IEEE 802.3at standard PoE, which can realize 80-100 meters of network cable power supply, and the ceiling-mounted shell design is convenient for installation. BL608X supports Wave 2 of MU-MIMO (Multiple User Multiple Input Multiple Output) technology and supports Mesh networking.
01
Product characteristics
www.sailskywifi.com

## Slide 5
02
Packing list
www.sailskywifi.com
BL608X ×1
Cable×1
（1 meter）
Product specification×1

## Slide 6
1. Office, classroom and other indoor places
03
Application scenarios
2. Shopping malls, supermarkets and other places
www.sailskywifi.com

## Slide 7
3 . Restaurants, cafes and other places
4. Hotel and other places
www.sailskywifi.com

## Slide 8
System information | 
Product Description | IEEE2x211n/ac/ax Dual Band Dual Concurrent Access Point
CPU | IPQ5018+6102+8337
Frequency | 2.4g&5g：
Flash Memory | SPI-NAND 128MB
DDR Memory | DDR3 512MB
Power consumption | 500mW
04
System information
www.sailskywifi.com
05
Gigabit Ethernet port
Gigabit Ethernet port | 
Gigabit Ethernet | LAN1: 10/100/1000 auto-sensing (MDI/MDX) RJ-45 (SFP optional) WAN1: 10/100/1000 auto-sensing (MDI/MDX) RJ-45
POE | LAN1 and WAN1: Gigabit ports operate as Powered Equipment (PD) within a standard 802.3at/af power supply (Ethernet) from a mid- or end-span Power Supply Equipment (PSE).

## Slide 9
Radio | 
1x2x2bg, 2.4GHz radio subsystem | IEEE802.11b/g/n/ac/ax MIMO 2x2 2.4~2.4835GHz -modulation IEEE802.11b/g: dsss (dbpsk, dqpsk, cck) OFDM (bpsk, qpsk, 16-qam, 64-qam) IEEE802.11n: OFDM (bpsk, qpsk, 16-qam, 64-qam) IEEE802.11ac: OFDM (bpsk, qpsk, 16-qam, 64-qam, 256-qam) IEEE802.11ax: OFDM (bpsk, qpsk, 16-qam, 64-qam, 256-qam, 1024-qam) - channel IEEE802.11b/g: Operation in channels 1-14 IEEE802.11n: HT20 and HT40. -Data rate: IEEE11b: 11/5.5/2/1Mbps IEEE11g: 54/48/36/24/18/12/9/6Mbps IEEE11n: 20MHz: 6.5Mbps~144.44Mbps 40MHz: 13.5Mbps~300Mbps IEEE11ac: 20MHz: 6.5Mbps~173.3Mbps 40MHz: 13.5Mbps~400Mbps IEEE11ax: 20MHz: 8.6Mbps~286.8Mbps 40MHz: 17.2Mbps~573.5Mbps TX power: 19dBm (maximum) (see table for details)
06
Radio
www.sskycn.com

## Slide 10
Radio | 
1x2x2a/n/ac5GHz radio subsystem PCI-e module | -IEEE802.11a/n/ac/ax MIMO 2x2 5.15~5.850GHz -modulation IEEE802.11a/n: OFDM (bpsk, qpsk, 16-qam, 64-qam) IEEE802.11ac OFDM (bpsk, qpsk, 16-qam, 64-qam, 256-qam) IEEE802.11ax: OFDM (bpsk, qpsk, 16-qam, 64-qam, 256-qam, 1024-qam) - channel IEEE802.11a: Operation in 36-165 channels IEEE802.11n: HT20 and HT40 IEEE802.11ac: HT20, HT40 and HT80 IEEE802.11ax: HT20, HT40 and HT80 - Data rate: IEEE11a: 54/48/36/24/18/12/9/6Mbps IEEE11n: 20MHz: 6.5Mbps~144.44Mbps 40MHz: 13.5Mbps~300Mbps 11ac: 20MHz: 6.5Mbps~173.3Mbps 40MHz: 13.5Mbps~400Mbps 80MHz: 29.3Mbps~867Mbps IEEE11ax: 20MHz: 8.6Mbps~286.8Mbps 40MHz: 17.2Mbps~573.5Mbps 80MHz: 36Mbps~1201Mbps TX power: 17dBm (maximum) (see table for details)
06
Radio
www.sailskywifi.com

## Slide 11
www.sskycn.com
07
LED
LED | 
WAN/LAN port indicator | 2*Green LED
LED | Wifi light ,system light
Tuya module | Reserve ZS3L module, using UART3
power consumption | ≤19.5W
08
09
Power supply
Environmental parameters
LED | 
DC power adapter | 100~240VAC, 50/60Hz input, Output: 12V/1.5A
PoE | 802.3at 48VDC PoE
Environmental parameters | 
EMI | -FCC part 15 Class B -CE
Safety | -ul60950-1 -EN60601
Temperature | -10 to 45 degrees Celsius (operating temperature) -40 to 85 degrees Celsius (storage temperature)
Operating humidity | 0% ~ 100% 无凝结
air pressure requirements | Altitude 3000m

## Slide 12
Authentication | 
Authentication | CCC，SRRC，CE，FCC
National Customer Service Number ：0755 - 27209470
Shenzhen Shuotian Information Technology Co., Ltd
5B-18, Shenzhou Computer Building, No.2 Beier Road, Longgang District, Shenzhen
Web：www.sskycn.com
E-mail：lin@sskycn.com
Tel：+86-13631482895
PC：518000
www.sailskywifi.com
10
Authentication
11
Other connectors and designs
Other connectors and designs | 
Reset/WPS Key | SW reset
Size | 260mm*220mm*45mm
Weight | 0.65kg

## Slide 13
Copyright©2020 硕天信息技术有限公司，保留所有权利